## Slide 1: The Kernel Abstraction

## Slide 2: Main Points
Process concept
  A process is the OS abstraction for executing a program with limited privileges
Dual-mode operation: user vs. kernel
  Kernel-mode: execute with complete privileges
  User-mode: execute with fewer privileges
Types of Mode Transfer
  What causes the processor to switch control from a user-level program to the kernel
Safe control transfer
  How do we switch from one mode to the other?

## Slide 3: Process Abstraction
Process: an instance of a program, running with limited rights
  Process vs Program
  Process Control Block (PCB)
  Thread: a sequence of instructions within a process
    Potentially many threads per process (for now 1:1)
  Address space: set of rights of a process
    Memory that the process can access
    Other permissions the process has (e.g., which system calls it can make, what files it can access)

## Slide 4: Process Creation

## Slide 5: Hardware Support: Dual-Mode Operation
Kernel mode
  Execution with the full privileges of the hardware
  Read/write to any memory, access any I/O device, read/write any disk sector, send/read any packet
User mode
  Limited privileges
  Only those granted by the operating system kernel
  The interpreter checks if a process has permission to perform each instruction

## Slide 6: A Model of a CPU

## Slide 7: A CPU with Dual-Mode Operation

## Slide 8: Hardware Support: Dual-Mode Operation
Privileged instructions
  Available to kernel
  Not available to user code
Limits on memory accesses
  To prevent user code from overwriting the kernel
Timer
  To regain control from a user program in a loop
Safe way to switch from user mode to kernel mode, and vice versa

## Slide 9: Privileged instructions
Should programs directly change their privilege level?
  No! for process isolation
  Possible indirectly through system calls
    But can transfer control into the OS kernel
Privileged Instructions
  Run by OS kernel
    Change privilege levels
    Adjust memory access
    Disable/enable interrupts

## Slide 10: Privileged instructions
Examples?
  Change mode bit in EFLAGs register!
  Change which memory locations a user program can access
  Send commands to I/O devices
  Read data from/write data to I/O devices
  Jump into kernel code
What could happen if an application attempts to access restricted memory or change its privilege?
  Processor exception->kernel exception handler
What could happen if applications were allowed to jump into kernel mode at any location in the kernel?
  Kernel verifies whether the user has the permission

## Slide 11: Simple Memory Protection
OS must make sure each application process can read/write only its own memory

## Slide 12: Towards Virtual Addresses
Problems with base and bounds?
  Expandable heap?
  Expandable stack?
  Memory sharing between processes?
    Multiple processes running the same program or using the same library
  Physical memory addresses
    Must change every instruction and data location each time the program is loaded into memory
  Memory fragmentation
    Difficult to relocate programs once started

## Slide 13: Virtual Addresses
All process memory starts at the same place, e.g., zero
  Virtual addresses never change
Each process thinks that it has the entire machine -> Transparent!
Actual physical memory locations determined at run-time

## Slide 14: Virtual Addresses
Translation done in hardware, using a table
Table set up by operating system kernel
Stack and heap start from separate ends

## Slide 15: Example
int staticVar = 0; // a static variable
main() {
staticVar += 1;
sleep(10); // sleep for x seconds
printf ("static address: %x, value: %d\n", &staticVar, staticVar);
}
What happens if we run two instances of this program at the same time?

## Slide 16: Question
With an object-oriented language and compiler, only an object’s methods can access the internal data inside an object. If the operating system only ran programs written in that language, would it still need hardware memory address protection?
  In theory, no
  In practice, yes
  Google Chrome example

## Slide 17: Hardware Timer
Hardware device that periodically interrupts the processor
  Returns control to the kernel handler
  Interrupt frequency set by the kernel
    Not by user code!
  Interrupts can be temporarily deferred
    Not by user code!
    Interrupt deferral crucial for implementing mutual exclusion
  How does the kernel know if an application is in an infinite loop?

## Slide 18: Mode Switch
From user mode to kernel mode
  Interrupts
    Asynchronous signal to the processor that some external event has occurred
    Saves the current execution state before executing at the interrupt handler at the kernel
    Interrupt handers are also specially designated
      Timer handler: Infinite loop alert
      I/O handler
      Interrupt vector table
      Inter-processor interrupts
    Triggered by timer and I/O devices
    Polling: kernel loops and checks events

## Slide 19: Mode Switch
From user mode to kernel mode
  Exceptions
    Triggered by unexpected program behavior
    Or malicious behavior!
    Divide by 0, access of non-existed or read-only memory
    OS halts process and return error coce
  System calls (aka protected procedure call)
    Request by program for kernel to do some operation on its behalf
    Only limited # of very carefully coded entry points
    Transparent: user applications do not know mode switch

## Slide 20: Mode Switch
From kernel mode to user mode
  New process/new thread start
    Jump to first instruction in program/thread
  Return from interrupt, exception, system call
    Resume suspended execution
  Process/thread context switch
    Resume some other process
  User-level upcall (UNIX signal)
    Asynchronous notification to user program

## Slide 21: How do we take interrupts safely?
Interrupt vector
  Limited number of entry points into kernel
Atomic transfer of control
  Single instruction to change:
    Program counter
    Stack pointer
    Memory protection
    Kernel/user mode
Transparent restartable execution
  User program does not know interrupt occurred

## Slide 22: Interrupt Vector
Table set up by OS kernel; pointers to code to run on different events

## Slide 23: Interrupt Stack
When context switch happens, the hardware changes its stack pointer to the base of the kernel’s interrupt stack and saves interrupted process’s registers by pushing them into the interrupt stack.
  Reverse operation when returning from the interrupt
Per-processor, located in kernel (not user) memory
  Usually a process/thread has both: kernel and user stack
Why can’t the interrupt handler run on the stack of the interrupted user process?

## Slide 24: Interrupt Stack
Page 66 for details

## Slide 25: Interrupt Masking
Interrupt handler runs with interrupts off
  Re-enabled when interrupt completes
OS kernel can also turn interrupts off
  Eg., when determining the next process/thread to run
  On x86
    CLI: disable interrrupts
    STI: enable interrupts
    Only applies to the current CPU (on a multicore)
We’ll need this to implement synchronization in chapter 5

## Slide 26: Interrupt Handlers
Non-blocking, run to completion
  Minimum necessary to allow device to take next interrupt
  Any waiting must be limited duration
  Wake up other threads to do any real work
    Linux: semaphore
Rest of device driver runs as a kernel thread

## Slide 27: At end of handler
Handler restores saved registers
Atomically return to interrupted process/thread
  Restore program counter
  Restore program stack
  Restore processor status word/condition codes
  Switch to user mode

## Slide 28: Upcall: User-level event delivery
Notify user process of some event that needs to be handled right away
  Time expiration
    Real-time user interface
    Time-slice for user-level thread manager
  Interrupt delivery for VM player
  Asynchronous I/O completion (async/await)
AKA UNIX signal

## Slide 29: Upcalls vs Interrupts
Signal handlers = interrupt vector
Signal stack = interrupt stack
Automatic save/restore registers = transparent resume
Signal masking: signals disabled while in signal handler

## Slide 30: Upcall: Before

## Slide 31: Upcall: During

## Slide 32
Page 75 for details

## Slide 34: User-Level Virtual Machine
How does VM Player work?
  Runs as a user-level application
  How does it catch privileged instructions, interrupts, device I/O?
Installs kernel driver, transparent to host kernel
  Requires administrator privileges!
  Modifies interrupt table to redirect to kernel VM code
  If interrupt is for VM, upcall
  If interrupt is for another process, reinstalls interrupt table and resumes kernel