## Slide 1: Storage Systems
Notes: Relative to book, I included more material on the physics of the disk head
Mentioned that disk and flash device has a CPU in it – it needs it for the complex reasoning it needs to make; e.g., disk head scheduling is now done by the disk device itself, as is remapping. Disks in very olden times very smart – because the CPU was insanely expensive. When CPU’s were moderately expensive, then I/O devices became dumb – so that you could build a cheaper overall system, the file system had to do more work. Now, the CPU is very cheap, so can include more intelligence on the device.
Or even, have a network appliance that appears like a disk, but is actually a CPU, a set of disks, and a bunch of clever algorithms.
Worth including material on error correcting codes here, I think
And we should update to a newer disk example
Also, the algebra for the 80% power point needed a bit more explanation (why multiply on the left hand side)

## Slide 2: Main Points
File systems
  Useful abstractions on top of physical devices
Storage hardware characteristics
  Disks and flash memory
File system usage patterns

## Slide 3: File Systems
Abstraction on top of persistent storage
  Magnetic disk
  Flash memory (e.g., USB thumb drive)
Devices provide
  Storage that (usually) survives across machine crashes
  Block level (random) access
  Large capacity at low cost
  Relatively slow performance
    Magnetic disk read takes 10-20M processor instructions

## Slide 4: File System as Illusionist: Hide Limitations of Physical Storage
Persistence of data stored in file system:
  Even if crash happens during an update
  Even if disk block becomes corrupted
  Even if flash memory wears out
Naming:
  Named data instead of disk block numbers
  Directories instead of flat storage
  Byte addressable data even though devices are block-oriented
Performance:
  Cached data
  Data placement and data structure organization
Controlled access to shared data

## Slide 5: File System Abstraction
File system
  Persistent, named data
  Hierarchical organization (directories, subdirectories)
  Access control on data
File: named collection of data
  Linear sequence of bytes (or a set of sequences)
  Read/write or memory mapped
Crash and storage error tolerance
  Operating system crashes (and disk errors) leave file system in a valid state
Performance
  Achieve close to the hardware limit in the average case

## Slide 6: Storage Devices
Magnetic disks
  Storage that rarely becomes corrupted
  Large capacity at low cost
  Block level random access
  Slow performance for random access
  Better performance for streaming access
Flash memory
  Storage that rarely becomes corrupted
  Capacity at intermediate cost (50x disk)
  Block level random access
  Good performance for reads; worse for random writes

## Slide 7: Magnetic Disk
Notes: Mentioned that disk and flash device has a CPU in it – it needs it for the complex reasoning it needs to make; e.g., disk head scheduling is now done by the disk device itself, as is remapping. Disks in very olden times very smart – because the CPU was insanely expensive. When CPU’s were moderately expensive, then I/O devices became dumb – so that you could build a cheaper overall system, the file system had to do more work. Now, the CPU is very cheap, so can include more intelligence on the device.

## Slide 8
Notes: Head and track are not to scale – head is actually much much bigger than a track.
Track ~ 1 micron wide
  Wavelength of light is ~ 0.5 micron
  Resolution of human eye: 50 microns
  Outer edge of disk is travelling at 30 mph, with the head riding on top of the disk surface with a cushion of a few atoms

## Slide 9: Disk Tracks
~ 1 micron wide
  Wavelength of light is ~ 0.5 micron
  Resolution of human eye: 50 microns
  100K tracks on a typical 2.5” disk
Separated by unused guard regions
  Reduces likelihood neighboring tracks are corrupted during writes (still a small non-zero chance)
Track length varies across disk
  Outside: More sectors per track, higher bandwidth
  Disk is organized into regions of tracks with same # of sectors/track
  Only outer half of radius is used
    Most of the disk area in the outer regions of the disk

## Slide 10: Sectors
Sectors contain sophisticated error correcting codes
  Disk head magnet has a field wider than track
  Hide corruptions due to neighboring track writes
Sector sparing
  Remap bad sectors transparently to spare sectors on the same surface
Slip sparing
  Remap all sectors (when there is a bad sector) to preserve sequential behavior
Track skewing
  Sector numbers offset from one track to the next, to allow for disk head movement for sequential ops
Notes: Error correcting code: ex: parity. But you can get more sophisticated.

## Slide 11: Disk Performance
Disk Latency =
  Seek Time + Rotation Time + Transfer Time
  Seek Time: time to move disk arm over track (1-20ms)
    Fine-grained position adjustment necessary for head to “settle”
    Head switch time ~ track switch time (on modern disks)
  Rotation Time: time to wait for disk to rotate under disk head
    Disk rotation: 4 – 15ms (depending on price of disk)
    On average, only need to wait half a rotation
  Transfer Time: time to transfer data onto/off of disk
    Disk head transfer rate: 50-100MB/s (5-10 usec/sector)
    Host transfer rate dependent on I/O connector (USB, SATA, …)

## Slide 12: Toshiba Disk (2008)

## Slide 13: Question
How long to complete 500 random disk reads, in FIFO order?

## Slide 14: Question
How long to complete 500 random disk reads, in FIFO order?
  Seek: average 10.5 msec
  Rotation: average 4.15 msec
  Transfer: 5-10 usec
500 * (10.5 + 4.15 + 0.01)/1000 = 7.3 seconds

## Slide 15: Question
How long to complete 500 sequential disk reads?

## Slide 16: Question
How long to complete 500 sequential disk reads?
  Seek Time: 10.5 ms (to reach first sector)
  Rotation Time: 4.15 ms (to reach first sector)
  Transfer Time: (outer track)
    500 sectors * 512 bytes / 128MB/sec = 2ms
Total: 10.5 + 4.15 + 2 = 16.7 ms
  Might need an extra head or track switch (+1ms)
  Track buffer may allow some sectors to be read off disk out of order (-2ms)

## Slide 17: Question
How large a transfer is needed to achieve 80% of the max disk transfer rate?

## Slide 18: Question
How large a transfer is needed to achieve 80% of the max disk transfer rate?
  Assume x rotations are needed, then solve for x:
  0.8 (10.5 ms + (1ms + 8.5ms) x) = 8.5ms x
Total: x = 9.1 rotations, 9.8MB

## Slide 19: Disk Scheduling
FIFO
  Schedule disk operations in order they arrive
  Downsides?

## Slide 20: Disk Scheduling
Shortest seek time first
  Not optimal!
    Suppose cluster of requests at far end of disk
  Downsides?

## Slide 21: Disk Scheduling
SCAN: move disk arm in one direction, until all requests satisfied, then reverse direction
Also called “elevator scheduling”

## Slide 22: Disk Scheduling
CSCAN: move disk arm in one direction, until all requests satisfied, then start again from farthest request

## Slide 23: Disk Scheduling
R-CSCAN: CSCAN but take into account that short track switch is < rotational delay

## Slide 24: Question
How long to complete 500 random disk reads, in any order?

## Slide 25: Question
How long to complete 500 random disk reads, in any order?
  Disk seek: 1ms (most will be short)
  Rotation: 4.15ms
  Transfer: 5-10usec
Total: 500 * (1 + 4.15 + 0.01) = 2.2 seconds
  Would be a bit shorter with R-CSCAN
  vs. 7.3 seconds if FIFO order

## Slide 26: Question
How long to read all of the bytes off of a disk?

## Slide 27: Question
How long to read all of the bytes off of a disk?
  Disk capacity: 320GB
  Disk bandwidth: 54-128MB/s
Transfer time =
  Disk capacity / average disk bandwidth
  ~ 3500 seconds (1 hour)

## Slide 28: File System Workload
File sizes
  Are most files small or large?
  Which accounts for more total storage: small or large files?

## Slide 29: File System Workload
File sizes
  Are most files small or large?
    SMALL
  Which accounts for more total storage: small or large files?
    LARGE

## Slide 30: File System Workload
File access
  Are most accesses to small or large files?
  Which accounts for more total I/O bytes: small or large files?

## Slide 31: File System Workload
File access
  Are most accesses to small or large files?
    SMALL
  Which accounts for more total I/O bytes: small or large files?
    LARGE

## Slide 32: File System Workload
How are files used?
  Most files are read/written sequentially
  Some files are read/written randomly
    Ex: database files, swap files
  Some files have a pre-defined size at creation
  Some files start small and grow over time
    Ex: program stdout, system logs

## Slide 33: File System Design
For small files:
  Small blocks for storage efficiency
  Concurrent ops more efficient than sequential
  Files used together should be stored together
For large files:
  Storage efficient (large blocks)
  Contiguous allocation for sequential access
  Efficient lookup for random access
May not know at file creation
  Whether file will become small or large
  Whether file is persistent or temporary
  Whether file will be used sequentially or randomly

## Slide 34: File System Abstraction
Directory
  Group of named files or subdirectories
  Mapping from file name to file metadata location
Path
  String that uniquely identifies file or directory
  Ex: /cse/www/education/courses/cse451/12au
Links
  Hard link: link from name to metadata location
  Soft link: link from name to alternate name
Mount
  Mapping from name in one file system to root of another

## Slide 35: UNIX File System API
create, link, unlink, createdir, rmdir
  Create file, link to file, remove link
  Create directory, remove directory
open, close, read, write, seek
  Open/close a file for reading/writing
  Seek resets current position
fsync
  File modifications can be cached
  fsync forces modifications to disk (like a memory barrier)